Archphile Manual
V.0.1

(minimum requirements – Archphile 0.99.72 alpha)

Authored by Mike Andonov
info@archphile.org

Table Of Contents

Introduction. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Finding The Ip Address For The First Time . . . . . . . . . . . . . . .
Connect Via SSH . . . . . . . . . . . . . . . . . . . . . . . . . . . .
File Editing with nano. . . . . . . . . . . . . . . . . . . . . . . . .
Systemd Services. . . . . . . . . . . . . . . . . . . . . . . . . . . .

1.0 System Configuration. . . . . . . . . . . . . . . . . . . . . . . .
1.1 Root Password . . . . . . . . . . . . . . . . . . . . . . . . . . .
1.2 Timezone And NTP Server Configuration . . . . . . . . . . . . . . .

2 Network Configuration . . . . . . . . . . . . . . . . . . . . . . . .

3.0 NAS Configuration . . . . . . . . . . . . . . . . . . . . . . . . .
3.1 Samba Shares. . . . . . . . . . . . . . . . . . . . . . . . . . . .
3.2 NFS Shares. . . . . . . . . . . . . . . . . . . . . . . . . . . . .
3.3 USB Disk Sharing. . . . . . . . . . . . . . . . . . . . . . . . . .

4.0 MPD . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
4.1 Packages. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
4.2 Additional File Extensions Support. . . . . . . . . . . . . . . . .
4.3 Software/Hardware Mixer . . . . . . . . . . . . . . . . . . . . . .
4.4 Resampling. . . . . . . . . . . . . . . . . . . . . . . . . . . . .
4.5 Library Auto Update . . . . . . . . . . . . . . . . . . . . . . . .
4.6 Backup/Restore Of Music Library Database. . . . . . . . . . . . . .

5.0 UPNP/DLNA Support . . . . . . . . . . . . . . . . . . . . . . . . .

6.0 Airplay Support . . . . . . . . . . . . . . . . . . . . . . . . . .

7.0 Spotify Support . . . . . . . . . . . . . . . . . . . . . . . . . .

8.0 Roon Support. . . . . . . . . . . . . . . . . . . . . . . . . . . .

9.0 Android Remote Control. . . . . . . . . . . . . . . . . . . . . . .

10.0 Archphile And I2S DACS For The Raspberry Pi. . . . . . . . . . . .

11.0 Archphile Optimization . . . . . . . . . . . . . . . . . . . . . .
11.1 Adroid C2 Optimizations. . . . . . . . . . . . . . . . . . . . . .
11.2 Raspberry Pi Optimizations . . . . . . . . . . . . . . . . . . . .
11.3 Generic Optimizations. . . . . . . . . . . . . . . . . . . . . . .

12.0 Real Life Examples . . . . . . . . . . . . . . . . . . . . . . . .
12.1 Simple Use With A USB Disk Or Stick. . . . . . . . . . . . . . . . . .
12.2 Simple Use With A NAS. . . . . . . . . . . . . . . . . . . . . . .

13.0 Frequently Asked Questions . . . . . . . . . . . . . . . . . . . .

Introduction

Archphile is an ArchlinuxARM (https://archlinuxarm.org) based Linux distribution with additonal packages and configuration in order to transform your board to a k.i.s.s. (keep it simple, stupid!) computer transport.

It currently supports All Armv7/Armv8 Raspberry Pi and Odroid C2 devices.

Archphile uses MPD [Music Player Daemon](https://www.musicpd.org).

MPD is a media player that acts as a network server and needs a client to use it with.

Archphile uses YMPD (https://ympd.org) web client by default. However you can use it with any other available MPD client.

Below you will find most of the information needed in order to sucessfully configure your board with Archphile.

Please note that you will need to connect via ssh in order to apply all required changes.

Finding the IP address for the first time

In order to connect to your Archphile machine, you need to know the IP address. This can be done by using an android/ios app like fing (htttps:/www.fing.io), or via the web interface of your router.

If your system supports bonjour/avahi, then you can use http://archphile.local that all archphile machines listen to

After connecting for the first time, it’s strongly suggested to set up a static network ip.

Connect Via SSH

Connecting via ssh is pretty easy. If you use Windows you will need putty:

https://www.putty.org

Linux and Mac os X users can simply use a terminal application and connect (assumming that Archphile uses the ip 192.168.1.142) using the following command:

ssh root@192.168.1.142

File editing with nano

Another very useful tool is nano editor. Archphile configuration is based on plain text file editing. For this purpose you will need an editor. As an example, lets say you want to edit etc/mpd.conf file. All you need to do is:

nano /etc/mpd.conf

When you finish editing the file, press CTRL + X, then press y and ENTER and that’s it. Your edited file is now saved!

Systemd services

Most of the programs found in archhpile are handled via systemd services. Some useful commands are:

systemctl enable|reenable|disable|start|stop|restart <blabla>

where <blabla> canbe mpd, ympd, upmpdcli, shairport etc..

1.0 System Configuration

1.1 Root Password

The default password for root is archphile. It is strongly recommended that you change this password the firsr time you boot Archphile. This can be done using the following command

passwd

1.2 Timezone and NTP server configuration

Timezone/NTP default settings are set up for the country I live in. If you want to change them you will need to do the following:

rm /etc/localtime

and then link to the appropriate time zone.

ln -s /usr/share/zoneinfo/Europe/Athens /etc/localtime

The above command is just an example. If you want to explore all available locations, please use the following command:

ls -la /usr/share/zoneinfo

In order to change NTP servers, you will need to edit the following file:

rm /etc/ntp.conf

2.0 Network configuration

Default network configuration uses dhcp. It's strongly recommended to change to static ip. In order to do this you must edit the following file:

nano /etc/netctl/archphile-network

The active configuration by default (for DHCP) is the following

Description='A basic dhcp ethernet connection'
Interface=eth0
Connection=ethernet
IP=dhcp
ExecUpPost='/usr/bin/ntpd -gq || true'

Lets assume that the ip of your router is 192.168.1.1 and you want to use the static ip 192.168.1.142 for the Archphile machine. The first step is to comment the dhcp section. Now, uncomment the static ip network and change the ips to match your setup:

#Description='A basic dhcp ethernet connection'
#Interface=eth0
#Connection=ethernet
#IP=dhcp
#ExecUpPost='/usr/bin/ntpd -gq || true'

Description='A basic ethernet connection with static ip'
Interface=eth0
Connection=ethernet
IP=static
Address=('192.168.1.142/24')
Gateway='192.168.1.1'
ExecUpPost='/usr/bin/ntpd -gq || true'

Save with CTRL+X, then press Y and ENTER.
The last step is to reenable archphile-network:

netctl reenable archphile-network

Now reboot with:

systemctl reboot

3.0 NAS Configuration

3.1 Samba Shares

Archphile supports samba/cifs/nfs by default. However there is no automated tool to configure the NAS. The only needed action is the editing of the following file:

nano /etc/fstab

Example:

Lets assume that you use a NAS with a static IP 192.168.1.150.The folder served is music and it is configured as public. All you need to do for this case is edit fstab and put all this information in the “Public Share” example:

//192.168.1.150/music /mnt/nas-samba cifs vers=1.0,guest,ro,uid=mpd,gid=audio,iocharset=utf8,nolock,noauto,x-systemd.automount,x-systemd.device-timeout=10,sec=ntlm

If this share was not public, you would need to use the next example found in fstab and put your username and password:

//192.168.1.150/music /mnt/nas-samba cifs vers=1.0,username=yourusername,password=yourpassword,ro,uid=mpd,gid=audio,iocharset=utf8,nolock,noauto,x-systemd.automount,x-systemd.device-timeout=10,sec=ntlm

If you compare this line with the one found in fstab, you will notice that rsize and wsize are missing. I suggest you to do the same, unless you know what you are doing and you want to bybass default lines.

A reboot is needed for the changes to take effect:

systemctl reboot

3.2 NFS Shares

For a NAS using NFS and a static IP of 192.168.1.150, the fstab section will be:

192.168.1.150:/music /mnt/nas-nfs nfs4 ro,noauto,x-systemd.automount,x-systemd.device-timeout=10,rsize=8192,wsize=8192

A reboot is needed for the changes to take effect:

systemctl reboot

3.3 USB Disk Sharing

If you use a usb disk with your board, you can use Archphile in order to serve it on your local network. All you need to do is the following:

systemctl start smbd nmbd
systemctl enable smbd nmbd

If you want to stop and disable this feature, you can use the following commands:

systemctl stop smbd nmbd
systemctl disable smbd nmbd

4.0 MPD

4.1 Packages

Archphile offers various MPD (Music Player Daemon) packages:

- mpd-archphile

this is the default Archphile package. It has most of the features needed for the average user. The major difference with other packages is that it has ffmpeg support, so that you can listen to alac or other exotic files.

- mpd-archphile-minimal

this is a stripped down version of the default file. Amongst others, it does not provide ffmpeg support.

- mpd-archphile-sacd

This package offers an MPD FORK with SACD ISO support.

All Archphile image come with mpd-archphile. If you want to install any of the rest you must do the following:

pacman -Sy mpd-archphile-minimal
systemctl reenable mpd
systemctl restart mpd

or

pacman -Sy mpd-archphile-sacd
systemctl reenable mpd
systemctl restart mpd

in order to re-install the officiall package:

pacman -Sy mpd-archphile
systemctl reenable mpd
systemctl restart mpd

4.2 Additional file extensions support (alac etc..)

Default MPD package (mpd-archphile) is built with ffmpeg support. This means that MPD can support additional file types like alac for example. All you need to do is enable ffmpeg in /etc/mpd.conf. You will find the following section:

nano /etc/mpd.conf

decoder {
plugin “ffmpeg”
enabled “no”
}

Change the no to yes:

decoder {
plugin “ffmpeg”
enabled “yes”
}

and restart MPD:

systemctl restart mpd

4.3 Software/Hardware mixer

Archphile comes with all mixers disabled by default in order to ensure bit perfect playback. However if you know what you are doing and you want to experiment, you can enable them in /etc/mpd.conf.

First you need to open mpd.conf file with an editor:

nano /etc/mpd.conf

and change the following line:

mixer_type	“disabled

to either

mixer_type	“hardware”

or

mixer_type	“software”

and restart MPD:

systemctl restart mpd

Please note that not all DACs support a hardware mixer (you can check with alsamixer for that..).

4.4 Resampling

MPD is built with SoX (http://sox.sourceforge.net/SoX/Resampling) Resampler and if you want to upsample/downsample, you will need to edit /etc/mpd.conf:

nano /etc/mpd.conf

Then, find this section:

#resampler {
# plugin "soxr"
# quality "very high"
#}

and enable it

resampler {
 plugin "soxr"
 quality "very high"
}

Next, go to audio_output section and find these lines:

#format "192000:24:2"

#format "*:24:*"

Let’s assume that you want to upsample everything to 24/192. You will just need to enable the first line.

format "192000:24:2"

If you want to upsample everything to 32/96, you will need to modify and enable the first line:

format "96000:32:2"

If you want to upsample everything to 32 bit, you will need to modify and enable the second line:

#format "*:32:*"

Save the new mpd.conf file and restart MPD with:

systemctl restart mpd

4.5 Library Auto Update

MPD database has an option for auto update. This means that MPD can scan for changes in library and add new files automatically. This is disabled by default.If you want to enable it you need to edit /etc/mpd.conf:

nano /etc/mpd.conf

and change:

auto_update “no”

to:

auto_update “yes”

and then restart MPD:

systemctl restart mpd

4.6 Backup/Restore of Music Library Database

IF you want to transfer your MPD library through installations, or simply keep a backup of it, you can use some pretty simple scripts I wrote: dbackup/drestore.

In order to backup the library,type:

dbackup

If you are using the same Archphile installation and you want to restore it, just type:

drestore

If you want to transfer your library database to a new installation, after using dbackup, use an application that supports SFTP file transfer like filezilla or winscp:

https://filezilla-project.org
https://winscp.net

and get mpd.db file from /opt/dbackup.

Now copy the new Archphile image on an sd card, boot to your new Archphile installation, and place the backed up mpd.db file in /opt/dbackup.

Now it’s time to restore:

drestore

and you ‘re ready to use your old library with MPD.

5.0 UPNP/DLNA Support

Archphile supports upnp/dlna protocol using upmpdcli:

https://www.lesbonscomptes.com/upmpdcli

Using upmpdcli, Archphile acts as a upnp/dlna renderer that can be used with various applications, like for example bubbleupnp.

Upmpdcli is not enabled by default. In order to start it you will need the following command:

systemctl start upmpdcli

If you want to enable it so that it runs after every boot:

systemctl enable upmpdcli

If you change your mind and you want to disable it again you can use the following command:

systemctl disable upmpdcli

6.0 Airplay Support

Archpile supports Airplay with the use of shairport-sync:

https://github.com/mikebrady/shairport-sync

shairport-sync is not enabled by default. In order to start it you will need the following command:

systemctl start shairport-sync

If you want to enable it so that it runs after every boot:

systemctl enable shairport-sync

If you change your mind and you want to disable it again you can use the following command:

systemctl disable shairport-sync

7.0 Spotify Support

Archphile supports Spotify, using librespot:

https://github.com/librespot-org

librespot works with the official Spotify applications, where Archphile will appear as a supported device. In order to configure librespot you will need to edit the following file:

nano etc/default/librespot

and put your username and password.

librespot is not enabled by default. In order to start it you will need the following command:

systemctl start librespot

If you want to enable it so that it runs after every boot:

systemctl enable librespot

If you change your mind and you want to disable it again you can use the following command:

systemctl disable librespot

8.0 Roon Support

Archphile can be used as a Roon bridge. The needed software is not open source and this is the reason that it’s not installed by default. If you want to use Archphile as a Roon Bridge you will need to install it:

For the Raspberry Pi you will need the following command:

pacman -Sy roonbridge-archhpile-arm7

For Odroid C2 you will need:

pacman -Sy roonbridge-archhpile-arm8

Roonbridge will not be enabled by default. In order to start it you will need the following command:

systemctl start roonbridge
If you want to enable it so that it runs after every boot:

systemctl enable roonbridge

If you change your mind and you want to disable it again you can use the following command:

systemctl disable roonbridge

9.0 Android Remote Control

In order to control various Archphile services, it’s highly suggested to create a custom SSH remote control (after setting up a static IP!). This can be done with an app like Raspberry SSH LITE (or the paid version). There you can create buttons for the majority of the services described above so that you don’t have to enable them (and run after each boot) if you don’t use them frequently. Below you will find examples of such buttons you can create:

– Start Spotify: add a button with this name and in the field of the command put systemctl start librespot

– Stop Spotify: add a button with this name and in the field of the command put systemctl stop librespot

– Start Upnp: add a button with this name and in the field of the command put systemctl start upmpdcli

– Stop Upnp: add a button with this name and in the field of the command put systemctl stop upmpdcli

– Start Shairport-sync: add a button with this name and in the field of the command put systemctl start shairport-sync

– Stop Shairport-sync: add a button with this name and in the field of the command put systemctl stop shairport-sync

You can do the same for Roonbridge.

In addition you vcan create some MPD related commands:

 - Restart MPD: add a button with this name and in the field of the command put systemctl restart mpd

– Update MPD library: add a button with this name and in the field of the command put mpc update

– Stop music: add a button with this name and in the field of the command put mpc stop
– Play music: add a button with this name and in the field of the command put mpc play

Last but not least, create a shutdown and a reboot button:

– Shutdown: add a button with this name and in the field of the command put systemctl poweroff

– Reboot: add a button with this name and in the field of the command put systemctl reboot

The advantage of this SSH remote is that you can control most of the functions of Archphile, without the need of terminal access. In addition you won’t need to enable any service you don’t need to run every time. For example, you will only use spotify when you want. When you don’t use it, librespot will not be enabled and it will not get any system resource.
10.0 Archphile and I2s DACs for the Raspberry Pi

The use of I2s DACs in Archphile is pretty simple and straight-forward. The only step needed is the editing of config.txt:

nano /boot/config.txt

There you will find a list of (disabled) ovelays for various I2S DACs. Lets assume you want to enable your Mamboberry Dac. You need to find this section:

# Hifiberry and Mamboberry Dacs
#dtoverlay=hifiberry-dac

enable the overlay:

# Hifiberry and Mamboberry Dacs
dtoverlay=hifiberry-dac

and reboot:

systemctl reboot

11.0 Archphile Optimization

11.1 Odroid C2 optimizations

Archphile for Odroid C2 comes with various optimizations enabled by default. Below you will find some useful information about the most important ones.

11.1.1 CPU Cores Isolation

The Odroid C2 Archphile image comes with cores 1,2 and 3 isolated by default.

Core 2 is used only by MPD, cores 3 and 4 are used for USB and ethernet interrupts. The remaining processes are handled by core 0.

The core isolation is achieved via the editing of /boot/boot.txt file (plus mkscr command):

nano boot/boot.txt

There you will find the appropriate configuration already applied with the isolcpus option:

setenv bootargs "console=ttyAML0,115200n8 root=PARTUUID=${uuid} isolcpus=1,2,3 rw rootwait earlycon"

The redirection of MPD so that it uses the core 1 is handled via a command in archphile-optimize script:

nano usr/bin/archphile-optimize

There you will find the following enabled command:

taskset -c -a -p 1 $(pidof mpd)

Please note that you don’t have to do anything from your side. All the information above is just given for you to be fully aware on what’s configured on your system.

11.1.2 CPU Affinity

By default USB inrerrupts are redirected to the core 4 and ethernet interrupts to core 3.The script including the appropriate commands is /usr/bin/irq-archphile.

The above script is then called by archphile-optimize which runs at every boot. If you edit it:

nano usr/bin/archphile-optimize

you will find the already enabled section:

# IRQ affinity optimization - Do not apply it if you have a Raspberry Pi!!!
/usr/bin/irq-archphile

Again, you don’t have to do anything as everything is already applied.

11.1.3 Odroid C2 optimizations mpd-archphile-sacd

As already mentioned, you have the option to install mpd-archphile-sacd, an MPD fork that supports SACD ISOs. As DTS decoding is very CPU hungry, if you decide to use this MPD fork, you will need to disable CPU isolation and MPD redirection.

Firstly you will need to edit boot/boot.txt:

nano /boot/boot.txt

Then find the line that includes isolcpus command:

setenv bootargs "console=ttyAML0,115200n8 root=PARTUUID=${uuid} isolcpus=1,2,3 rw rootwait earlycon"

and get rid of it:

setenv bootargs "console=ttyAML0,115200n8 root=PARTUUID=${uuid} rw rootwait earlycon"

then give the following two commands:

cd /boot

./mkscr

Then edit archphile-optimize:

nano /usr/bin/archphile-optimize

find this command:

taskset -c -a -p 1 $(pidof mpd)

and disable it:

#taskset -c -a -p 1 $(pidof mpd)

As a last step, reboot:

systemctl reboot

11.2 Raspberry Pi optimizations

11.2.1 CPU Cores Isolation

The Raspberry Pi Archphile image comes with cores 0 and 1 are isolated by default.

Core 0 handles all interupts (that unfortunately cannot be redirected in RPI) and core 1 is only used by MPD. Everything else is handled by cores 2 and 3.

The core isolation is achieved via the editing of /boot/comdline.txt file:

nano /boot/cmdline.txt

There you will find the appropriate configuration already applied with the isolcpus option:

root=/dev/mmcblk0p2 rw rootwait console=ttyAMA0,115200 console=tty1 selinux=0 isolcpus=0,1 plymouth.enable=0 smsc95xx.turbo_mode=N dwc_otg.lpm_enable=0 kgdboc=ttyAMA0,115200 elevator=noop

The redirection of MPD so that it uses the core 1 is handled via a command in archphile-optimize script:

nano usr/bin/archphile-optimize

There you will find the following enabled command:

taskset -c -a -p 1 $(pidof mpd)

Please note that you don’t have to do anything from your side. All the information above is just given for you to be fully aware on what’s configured on your system.

11.2.2 Wireless, Bluetooth and HDMI

Wireless and bluetooth are disabled by default. If you want to enable them, you will need to edit /boot/config.txt:

nano /boot/config.txt

11.2.2.1 Wireless

If you want to enable wireless, you will need to find the following line:

dtoverlay=pi3-disable-wifi

and disable it:

#dtoverlay=pi3-disable-wifi

Please note that in order to use a wireless, you will neet to set a country code.
This can be done in archphile-optimize:

nano /usr/bin/archphile-optimize

find the line below

#iw reg set GR

change to your country’s code (you will have to google for wireless country codes) and enable. For example, for Norway the line will be:

iw reg set NO

Save and reboot:

systemctl reboot

11.2.2.2 Bluetooth

If you want to enable bluetooth you will need to find the following line:

dtoverlay=pi3-disable-bt

and disable it

#dtoverlay=pi3-disable-bt

As a last step, you will need to reboot:

systemctl reboot

11.2.2.3 HDMI

HDMI is enabled by default. If you want to disable it, you can edit archphile-optimize:

nano /usr/bin/archphile-optimize

find the section below

# Disable HDMI for RPI
#/opt/vc/bin/tvservice -o

and enable it

# Disable HDMI for RPI
/opt/vc/bin/tvservice -o

Finally reboot

systemctl reboot

11.2.3 Raspberry Pi optimizations mpd-archphile-sacd

As already mentioned, you have the option to install mpd-archphile-sacd, an MPD fork that supports SACD ISOs. As DTS decoding is very CPU hungry, if you decide to use this MPD fork, you will need to disable CPU isolation and MPD redirection.

Firstly you will need to edit boot/cmdline.txt:

nano /boot/boot.txt

disable the line that includes the isoclcpu command:

#setenv bootargs "console=ttyAML0,115200n8 root=PARTUUID=${uuid} isolcpus=1,2,3 rw rootwait earlycon"

and enable the “Default Configuration” Line:

#root=/dev/mmcblk0p2 rw rootwait console=ttyAMA0,115200 console=tty1 selinux=0 plymouth.enable=0 smsc95xx.turbo_mode=N dwc_otg.lpm_enable=0 kgdboc=ttyAMA0,115200 elevator=noop

Then, edit archphile-optimize:

nano /usr/bin/archphile-optimize

find this command:

taskset -c -a -p 1 $(pidof mpd)

and disable it:

#taskset -c -a -p 1 $(pidof mpd)

As a last step, reboot:

systemctl reboot

11.3 Generic Optimizations

If you never use YMPD and you prefer another MPD client, you can disable it with:

systemctl disable ympd

if you later change your mind and you want to enable it:

systemctl enable ympd

If you are sure that you don’t need avahi for bonjour network discovery, you can disable it with:

systemctl disable avahi-daemon

if you later change your mind and you want to enable it:

systemctl enable avahi-daemon

If you don’t have any USB disk/stick on Archphile and you don’t plan to use one, you can disable the usb automounter:

systemctl disable devmon@root

if you later change your mind and you want to enable it:

systemctl enable devmon@root

12.0 Real Life Examples

In this section I will analyze some of the most frequent user setups in order to show how easy it is to get started with Archphile.

12.1 Simple use with a USB disk or stick

Let’s assume that you have a USB disk or stick with your music files and that this device is plugged οn your Archphile board.

The first thing that you have to do is to find the IP address of thw Archphile device. As I already mentioned in the introduction of this manual, in order to do this, the simplest way is to use fing application for android or ios.

Now that you found the IP, you are ready to use your board!

Just open a web browser and type the IP you just found. What you will immediately see is the default Archphile MPD client, named YMPD:

IF your os supports bonjour/avahi, instead of using the IP, you can access the board just using the following address:

archphile.local

The next thing that you have to do is start updating the MPD database, so that MPD is able to scan your files. In order to do this, just go to YMPD “Settings” and press the button “Update Database”. After a while, your files will start appearing in the “Browse” section of YMPD.

Please note that depending on the size of the music library it might take from seconds to hours in order to complete.

When this procedure is over you can start browsing your library throught YMPD and choose the files that you want to listen to.

Although you can keep using Archphile like it was described above, seting a static IP is almost necessary. This way you will ensure that you will always know how to access your transport and in addition you will be able to use an SSH android remote. So the remaining steps to complete Archphile setup are:

- Follow the instructions of Chapter 2.0 (Network Configuration) in order to set a static IP
- Follow the instrucitons of Chapter 9.0 (Android Remote Control) in order set up an SSH remote

- As a last optional step you can install an MPD client (MPD Remote, M.A.L.P, MPDroid etc..) on your smartphone to use in addition to YMPD.

12.2 Simple use with a NAS

This scenario is almost identical to the one above. The only extra step you have to do, is to follow the instructions from Chapter 3.0 (Nas Configuration) and configure your NAS.

After you reboot, you will need to go to YMPD “Settings” and press the button “Update Database”. After a while, your files will start appearing in the “Browse” section of YMPD.

13.0 Frequently Asked Questions

- Is really Archphile a new Linux distribution?

No, Archphile is not a new distribution. It’s just ArchlinuxARM (https://archlinuxarm.org) with pre-installed default and custom packages, plus many additional tweaks and configuration.

Please note, that although being an ArchlinuxARM distribution, it’s not rolling release. Updating the system with pacman will 99,9% break the additional Archphile packages.

- I want to buy Archphile. How much does it cost?

Archphile is a completely free/open source software. You don’t have to pay anything in order to get it and use it. However if you are astisfied with this project, you can help it be kept alive by donating, using the paypal or BTC information on the right side of Archphile website (http://archphile.org)

- What are the benefits of using Archphile?

Archphile is mainly targeted to Raspberry Pi and Odroid C2 owners who want to use their devices as music transports and don’t have the knowledge or the time to spend in order to configure a Linux distribution for this purpose.

- I am using Volumio/Runeaudio/Moodeaudio. Why should I change and use Archphile

I don’t care what you are currently using. As long as you are satisfied with your distro stick on it and listen to your music.

- Come on dude! Give me a reason to prefer Archphile over the other distributions

Ok. The philosophy behind archphile is to keep it simple. You will configure the system once and forget it.

Archphile doesn’t use heavy web servers with php, mysql or whatever and it’s configured so that it uses the less possuble resources.

- Yes, but configuring Archphile is so difficult. YMPD does not have any system configuration settings. It even doesn’t have a shutdown button!

Yes configuring Archphile via terminal file editing might seem difficult for newbies and this is the reason I wrote this manual.

Regarding YMPD, yes it does not have any confuguration setting or shutdown button, because it’s just an MPC client. It’s job is to control MPD and nothing more.

- Do you really use Archphile as a transport for your hifi or do you just play around with it?

The reason for keep developing Archphile is because I am a user of it. I use an Odroid C2 with a 9018k2m DAC and my flacs are served via a diy USB NAS (DD-WRT Router with a USB disk on it) using SAMBA.

- You describe Archphile as an “audiophile” distribution. What do you mean with this term? Is it that good?

The term audiophile is usually used in order to describe people enthusiastic high fidelity sound reproduction.
I don’t state that using Archphile with a Raspberry Pi or an Odroid C2 is a high quality hi-fi or hi-end solution. To be honest with you I really don’t care about this! Archphileis a distribution for people that want to get the best out of these tiny boards with regards to audio reproduction and just start listening to music.

- I see that you focus very much on DSD capabilities, offering extra custom MPD fork packages. Why are you so much interested in this format? It it so good?

To be honest, I don’t like and I don’t listen to DSD files. Everything that has to do with DSD is a hype in my opinion.

I believe that a good redbook file (16/44.1) should be enough for a superb sound. The reason I play around with DSD, creating custom packages, etc. is because I am a geek and I like playing around with stuff like that.

- I want the X or Y feature to be included. Please can you do this?

No!

- I have a question and I need to contact you. How can I contact you?

Please send an email to info@archphile.org, but please, before you send me an email, Read The Fucking Manual!